## Slide 1: Harvest – Clean – Temper

## Slide 2
Notes: Where varieties of wheat are grown in the United States.

## Slide 3: Wheat Harvest in Kansas
Notes: https://www.youtube.com/watch?v=wmhg1qyhvvs

## Slide 4: Cleaning
What
Cleaning the wheat/seeds before milling
Why
dust control, sanitation, protect process equipment, produce quality product, remove foreign material
How
  Separator: Two decks of screens - size (removes larger than and smaller than wheat)
  Cylinder Separator: Two decks of screens – shape (removes weed seeds – barley, oats, soybeans, wild garlic)
  Infestation Destroyer: Friability – removes insect damaged/infested kernels
  Dust Control – product degradation/loss, endangerment of plant facilities and human health, worker discomfort, general housekeeping

## Slide 5: Tempering
What
Tempering: time given to allow water to absorb into kernels
  Adds up to 7% moisture in one temper step
Why
Mellows (softens) the endosperm
  increases flour extraction
  reduces power consumption and noise level of roller mills
  reduces flour ash content
Toughens the bran
  bran breaks up less and remains in bigger pieces
  large bran flakes can effectively have flour removed without grinding the bran
How
Conditioning
  Measure dry clean wheat moisture content
  Measure wheat for water
  Measure and add water
  Mix
  Temper (timing given to allow water to absorb)
Notes: *Harder wheat = longer temp time
Extraction = taking out of something

## Slide 6: Tempering
Tempering in Action
Seeds tempering (submerged) after 3 hours, 6 hours, 18 hours, and 24 hours

## Slide 8: Impact on Temper Time
Harder wheat = longer temper time
More vitreous = longer temper time
Cold wheat = longer temper time
Cold room = longer temper time
Low starting moisture content = longer temper time
High target moisture content = longer temper time
Which classes of wheat would have longer temper times?
Notes: *Vitreous = glassy, translucent

## Slide 9: Wheat Class Temper Times
Wheat Class | Target MC | Target Temper Time
Durum Wheat | 17% | 4-6 or 24-36
Hard Red Spring | 15.5-16.5% | 12-24 hours
Hard Red Winter | 15.5-16-5% | 12-18 hours
Soft Wheat Classes | 14.5-15% | 6-8 hours

## Slide 10: Tempering
Notes: https://www.youtube.com/watch?v=WsTvZXX2ddA
The following screenshots are from the Indian Institute of Food Processing Technology: Demonstration Video on Processing of Wheat Milling - English

## Slide 11: Tempering Process

## Slide 12: Tempering Process

## Slide 13: Tempering Process

## Slide 14: Tempering Process

## Slide 15: Tempering Process

## Slide 16: Tempering Process

## Slide 17: Tempering Process